## Slide 1
SCARES REPEATERS
NM5F/N5HC 10/18/2021
Current Status

## Slide 2
Caption

## Slide 3
Pajarito
Racked Equipment
Duplexer
Router
Repeater
Packet Radio
Power Supply
Link Interface
Caption

## Slide 4
La Madera
Racked Equipment
Router
Repeater
Link Interface
Duplexer
Batteries? TBD
Caption

## Slide 5
Rainbow
Racked Equipment
Duplexer (UHF)
Router
Repeaters
Power Supply
Link Interfaces
Duplexer UHF
Caption

## Slide 6
Rainbow
Repeater TX Performance
 | Transmitter Rated Power w/Load
Transmitter Frequency | 147.10000 MHz
Code Plug Tx Power Out (Watts) | 25
Rated Power Meaasured w/Load | 22.3 Watts
Corrected Rated Power w/Load | 25.1 Watts
 | Transmitter Frequency Alignment
Tx Freq. Error Found | 15.00 Hz
Tx Freq. Error Adjusted | 15.00 Hz
 | Transmitter Performance
Deviation (Analog only) | 2.50 kHz
Internal Reference | Operational

## Slide 7
Rainbow
System TX Performance
 | Power Output
Code Plug Tx Power Out | 25 Watts (25 Watts)
Station Power Output | 22.3 Watts
Station Reflected Power | 0.2 Watts
Corrected Station Power | 25.1 Watts
 | Duplexer
Duplexer Input | 25.1 Watts
Duplexer Output | 12.5 Watts
Duplexer Reflected Pwr | 0.2 Watts
Corrected Duplexer Output | 14.1 Watts
Duplexer Loss | -2.51 dB (-2.2 dB)
 | Final Power to Antenna
Final CP Tx Power Out (Watts) | 25
Forward Power to Antenna | 12.5 Watts
Antenna Reflected Power | 0.2 Watts
Corrected Antenna Power | 14.1 Watts

## Slide 8
Rainbow
Repeater RX Performance
 | Receiver Internal Test
Receiver Frequency | 147.70000 MHz
Receiver Test Result | Pass
 | Receiver Performance
 | Receiver Sensitivty (12dB SINAD)
Receiver Sensitivity | -116.50 dBm (-117.3)
Rx Corrected Sensitivity | -117.00 dBm
 | Duplexer Performance
Duplexer Sens. | -113.00 dBm
Duplexer Corrected Sensitivity | -113.50 dBm
Duplexer Loss | -3.5 dB (-2.2)
 | Carrier Squelch Alignment (Analog only)
Carrier Squelch Level (Analog) | 113.50 dBm

## Slide 9
Rainbow
System RX Performance
 | Receiver Environmental Impact
Sensitivity at Rx Ant. Input | -113.50 dBm
Load Sensitivity (Test A) | -72.00 dBm
Test A Corrected | -72.50 dBm
Environmental Effects (Test B) | -67.00 dBm
Test B Corrected | -67.50 dBm
Tx to Rx Desense (Test C) | -67.00 dBm
Effective Receiver Sensitivity | -108.5 dBm
Environmental Degradation | -5.0 dBm
Total Receiver System Loss | -3.5 dB
Environmental Color Legend: | Acceptable | Caution | Warning
1. Transmitter Desense | Desense < 5dB | Marginal TX Desense > 5dB < 15dB | High TX Desense > 15dB
2. Environmental Degradation | Degradation < 6dB | Marginal Degradation > 6dB < 18dB | High Degradation >18dB
Caption

## Slide 10
Rainbow
Un-Balance. Typical Amateur 2m Tranciver
-164 dB
-122dBm
42 dBm (14W)
47 dBm (50W)
-108 dBm
47 - 164 = -117
-108 -117 = -9dB
47dBm+9dB = 56dBm ~ 400W

## Slide 11
Rainbow
Un-balance.Typical Commercial 2m Tranciver
-161 dB
-119dBm
42 dBm
47 dBm
-108 dBm
47 - 161 = -114
-108 -117 = -6dB
47dBm+6dB = 56dBm = 200W

## Slide 12
Rainbow
Balance.Typical Commercial 2m Tranciver
-155 dB
-119dBm
36 dBm (5W)
47 dBm
-108 dBm
47 - 155 = -108
36dBm ~ 5W

## Slide 13
Rainbow
Optimization notes
Duplexer had some mismatch between the individual filters in the TX and RX chain. Duplexer are now at spec:
  Insert loss of -2.18dB
  Isolation < -105dB
  RX System now at -3.5dB (sensitivity) insert loss.
  Measuring with the VNA we have -2.25dB loss.
  Manufacturer suggest that some improvements could be achieved by using a cable in 1/2 wave increments

## Slide 14
Rainbow
Inventory
QTY | Make | Model | Location | Notes
1 | TBD | 40U 2 Post 19” Rack | Rainbow Communication Shelter | 
1 | Kenwood | TKR-750 | Rainbow Communication Shelter | VHF Repeater
1 | Kenwood | TKR-850 | Rainbow Communication Shelter | UHF Repeater
1 | TX RX | 28-37-11 E/G | Rainbow Communication Shelter | VHF Duplexer
1 | TBD | UHF Duplexer | Rainbow Communication Shelter | UHF Duplexer
2 | Micro Node | RTCM | Rainbow Communication Shelter | Link interfaces
2 | TBD | Raspberry pi | Rainbow Communication Shelter | Link Controller
1 | Mikrotik | RB2011 UAS-RM | Rainbow Communication Shelter | Router / Switch
1 | Astron | TBD | Rainbow Communication Shelter | Power Supply
200’ | Andrew | LDF4-50A | Rainbow Tower @ 180’ | 1/2” Heliax Coaxial Cable (VHF)
190’ | Andrew | LDF4-50A | Rainbow Tower @ 170’ | 1/2” Heliax Coaxial Cable (UHF)
1 | Andrew | DB224-A | Rainbow Tower @ 180’ | Four-bay exposed dipole VHF antenna
1 | Andrew | DB404-B | Rainbow Tower @ 170’ | Four-bay exposed dipole UHF antenna
1 | Mikrotik | RB912UAG-5HPnD | Rainbow Tower @ ~30’ | Link Radio

## Slide 15
Pajarito
Inventory
QTY | Make | Model | Location | Notes
1 | TBD | 40U 2 Post 19” Rack | Pajarito Communication Shelter | 
1 | Kenwood | TKR-850 | Pajarito Communication Shelter | UHF Repeater
1 | TX RX | 28-66-02A | Pajarito Communication Shelter | UHF Duplexer
1 | Micro Node | RTCM | Pajarito Communication Shelter | Link interfaces
1 | TBD | Raspberry pi | Pajarito Communication Shelter | Link Controller
1 | Mikrotik | RB2011 UAS-RM | Pajarito Communication Shelter | Router / Switch
1 | Astron | TBD | Pajarito Communication Shelter | Power Supply
1 | ICOM | TBD | Pajarito Communication Shelter | Packet Data VHF Transciver
1 | TBD | Raspberry pi | Pajarito Communication Shelter | Packet Data Controler
TBD | Andrew | LDF5-50A | Pajarito tower 10 feet below top | 7/8” Heliax Coaxial Cable (UHF)
1 | Andrew | DB404-B | Pajarito tower 10 feet below top | Four-bay exposed dipole UHF antenna
50’ | Times Microwave | LMR400 | Pajarito tower @ 30’ | 3/8” Low loss Coaxial cable (VHF)
1 | TBD | 1/4 Wave Vertical Antenna | Pajarito tower @ 30’ | VHF Vertical omni directional

## Slide 16
La Madera
Inventory
QTY | Make | Model | Location | Notes
1 | TBD | 40U 4 Post 19” Rack | Loft at La Madera VFD | 
1 | Kenwood | TKR-750 | Loft at La Madera VFD | VHF Repeater
1 | TX RX | 28-37-11 E/G | Loft at La Madera VFD | VHF Duplexer
1 | Micro Node | RTCM | Loft at La Madera VFD | Link interfaces
1 | TBD | Raspberry pi | Loft at La Madera VFD | Link Controller
1 | Mikrotik | RB2011 UAS-RM | Loft at La Madera VFD | Router / Switch
1 | Astron | TBD | Loft at La Madera VFD | Power Supply
60’ | Times Microwave | LMR400 | La Madera VFD old tower @ ~ 50’ | 3/8” Low loss Coaxial cable (VHF)
1 | Comet | TBD | La Madera VFD old tower @ ~ 50’ | Vertical 5/8 Wave Antenna
1 | Mikrotik | RB912UAG-5HPnD | La Madera VFD tower @ ~ 50’ | Link Radio

## Slide 17
Punch List
Rainbow
Replace LMR-400 cable between Duplexer and SPD.
  Braided over Foil creates PIM, degrades reception.
    Replace with corrugated 1/2” Super flex.
    Replace cables between Repeater and duplexer
      Cables have been cut and are ready to be swapped out.
Complete 443.0 repeater optimization.
Replace server.
  Server is sunset.
    +10 year old.
    Constant use over 7 years.
  Replace with Raspberry Pi 4
    Less cost than repairing a single (rotating 7200RPM) drive.

## Slide 18
Punch List
Pajarito
Start Repeater optimization.
Repair Packed Node
  New Controller is ready to be installed.

## Slide 19
Punch List
La Madera
Start Repeater optimization.
Replace LMR-400 cable.
  Braided over Foil creates PIM, degrades reception.
    Replace with corrugated 1/2” Heliax & Super flex.

## Slide 20
Linking
FD Backhaul
Re-establish link to Pajarito
  IP transport.
    Ethernet Handovers:
      Pajarito
      Rainbow
    Requested bandwidth:
      1Mbit/s
    No new network equipment required.

## Slide 21
Linking
Decommissions
Rainbow:
  Remove Placitas Link radio
Placitas
  Remove Rainbow Link Radio.
  Remove router
    Will be a spare part.
Sandoval Count IT (basement)
  Remove Server
    Sunset equipment.
  Remove Router
    New spare part.

## Slide 22
Rainbow
Un-Balance. Typical Amateur 2m Tranciver
-164 dB
-122dBm
42 dBm
47 dBm
-108 dBm
47 - 164 = -117
-108 -117 = -9dB
47dBm+9dB = 56dBm = 398W

## Slide 23
Rainbow
Un-balance.Typical Commercial 2m Tranciver
-161 dB
-119dBm
42 dBm
47 dBm
-108 dBm
47 - 161 = -114
-108 -117 = -6dB
47dBm+6dB = 56dBm = 200W

## Slide 24
Rainbow
Balance.Typical Commercial 2m Tranciver
-155 dB
-119dBm
36 dBm
47 dBm
-108 dBm
47 - 155 = -108
36dBm ~ 5W